## Slide 1: The Theory and Practice of Real-time PCR Part2: qPCR
Adam Northcutt
May 9th 2016

## Slide 2: Outline
Fundamentals of qPCR
  What is real-time PCR? How is it different?
  Designing a RT-qPCR assay
Performing a qPCR reaction
  Dilution Series
  Amplification plots
  Melt Curve
Analyzing qPCR data
  Absolute Quantitation
  Relation Quantitation

## Slide 6: The Various Types of PCR
The Polymerase Chain Reaction (PCR) is a method to amplify specific fragments of DNA.
  Wikipedia lists 26 different variations of PCR
  Most are simply manipulations of Endpoint PCR (standard PCR)
  qPCR
    Real-time measurements of DNA amplification
  Digital PCR
    Samples are partitioned into droplets where amplification takes place
      Droplets are measured for fluorescence, giving absolute quantitation w/out standards
Notes: Assembly PCR
Asymmetric PCR
Dial-out PCR
Nanoparticle-assisted PCR
Nested PCR
RT-PCR

## Slide 7: Real-time PCR Instruments
Must contain thermal cycling & fluorescence detection in one package

## Slide 8: What goes into a qPCR reaction?
DNA template
  cDNA, gDNA, pDNA
Taq polymerase
  Mg2+
  dNTPs
Reporter molecules
  Dyes or probes
Real-time primers

## Slide 9: Real-time primers
How are they different?
  Amplicon size = 75-125bp
Target sequence ideally is verified
  Sanger sequencing
  NCBI confirmed
  G-blocks
Primers should not be in highly conserved regions for families of genes
http://www.nature.com/mt/journal/v20/n7/fig_tab/mt201260t1.html

## Slide 10: Real-time PCR Chemistries
A fluorescent reporter is used to measure the amplification of DNA
  Two types of reporters:
  dsDNA binding dye Labeled primer or probe

## Slide 11: Dye-based qPCR
Dye intercalates with PCR product
  Free dye -> low fluorescence
  Bound dye -> high fluorescence
As more PCR product is produced, more dye is bound
Fluorescence is directly proportional to the amount of product
SYBR Green I
Absorbs blue light λ = 497nm
Emits green light λ = 520nm
Notes: SYBR green is a cyanine dye (absorbs blue), and there are multiple other kinds.
SYBR Green I binds to the minor groove of DNA
SYBR Gold
Oxazole Yellow (YO)
Thiazole Orange (TO)
PicoGreen (PG)
Ethidium bromide has been used, but isn’t as sensitive as some other dyes.

## Slide 13: Probe Based qPCR
Oligonucleotide with a reporter and a quencher
  Gene specific binding between forward and reverse primer
Both primers and probe anneal to target
  During extension, 5’ nuclease activity of Taq polymerase degrades probe.

## Slide 15: Probe-based methods allow multiplexing
Multiplexing is where multiple genes are amplified in the same reaction
  Allows for multiple targets and normalizer in same reaction
    Conserves sample

## Slide 16: What does the reaction look like?
RFU – Relative fluorescence units
Cycle – Each round of amplification
Baseline – Initial reporter fluorescence
Exponential phase – product is doubling each cycle
Plateau – product formation is diminishing
Notes: Amplification curve

## Slide 17: Generating a Standard Curve
Enough dilutions should be prepared to cover the entire expected range of expression for target
At least a 5 point 10-fold dilution series for generating standard curve
Include a no template control (NTC)
  qPCR mix with no added template

## Slide 18: Melt Curves
Once amplification is over, the temp at which the product melts is measured
  If all product is the same length, it will melt at the same temp, giving 1 peak

## Slide 19: Melt Curve

## Slide 20: Analyzing the amplification curve
Cq = quantification cycle
  Cycle number where amplification curve crosses threshold.
  Average of Cq called Ct
  Ct is inversely proportional to amount of starting material
    i.e., fewer cycles means more starting material

## Slide 21: Threshold
Typically set at 10 standard deviations above baseline
Tells software where to find the Cycle threshold Ct
Can be adjusted up or down
Notes: This is a semi-log plot of amplification curves
Allows better visualization of amplification threshold crossing Cq

## Slide 22: Converting Ct values to quantity
Two approaches: Absolute and Relative Quantitation
Absolute (Standard Curve) Quantitation
  Use Ct to determine amount of target in unknown samples
    Based on standard curve from dilution series of known copies
Relative Quantitation
  Compare Ct values of target sample versus control sample – ΔCt
    Normalize target amount to internal references – ΔΔCt
    Usually 18s rRNA, beta-actin, GAPDH from same sample
Notes: Standard Curve Quantitation is only method that gives absolute copy numbers

## Slide 23: Standard Curve Quantitation
Plotted by Ct vs (log) concentration
Reaction efficiency is a function of the slope
  100% efficiency (theoretical max) means sample is doubling each cycle
Samples with unknown concentrations can have their Ct compared to the standard curve
Notes: Slopes more negative than -3.33 indicate reactions that are simply less than 100% efficiency, while samples more positive could be from pipetting errors or sample quality
Curve should have correlation coefficient (R squared value) greater than 0.99
When pipetted in triplicate, any one sample should have a standard deviation of less than 0.3, otherwise it is questionable and could be thrown out.

## Slide 24: Absolute Quantitation Calculations
Let’s say sample comes off at cycle 15 with a standard curve that gives this equation:
Quanitity = 10^ ((15 – 26.81)/-3.55)
Quantity = 2122
What if the Ct = 17?
Quantity = 580 (approx. 4 fold less)

## Slide 25: Relative Quantitation
Product formed after n number of cycles = 2n (at 100% efficiency)
Therefore, if two samples have a cycle threshold difference (ΔCt) of 1, they have a 2-fold difference in starting copies
If efficiency is not 100%, then it has to be corrected for.
Notes: Pfaffl method

## Slide 26: Normalization
A good normalizer gene will only vary in expression with changes in amount of original sample
  Not change with experimental conditions
Necessary to ensure that changes in gene expression are not due solely to sample quality variation

## Slide 28: Delta delta Ct Method
This is a relative measure of the change in the difference between a target gene and a reference gene between two samples
ΔCt = Ct(target) – Ct (reference)
Fold difference =
  ΔΔCt = 2^ (ΔCt of A – ΔCt of B)
  ΔΔCt = 2^(4)
  ΔΔCt = 16-fold difference
 | Target Ct | Reference Ct | ΔCt
Sample A (control) | 16 | 8 | 8
Sample B (treated) | 16 | 12 | 4
Pfaffl method to correct for efficiencies
Notes: Pfaffl method
requires that primer efficiency be known but needs to be determined only once with a standard curve or a different method
produces relative amount (e.g. treated is 2x untreated)

## Slide 29: 1- or 2-step RT-qPCR?
One-step RT-qPCR
  Requires only one reaction mix because RT and PCR occur in same tube
  May get better limit of detection with low-level transcripts
  Requires sequence-specific RT primer for cDNA synthesis
  Only specific transcripts can be investigated, and the rest is lost after reaction
Two-step RT-qPCR
  Two discrete reaction mixes (RT followed by PCR)
  cDNA can be stored for later reactions
  Random hexamer primers in the RT allows for all mRNAs & rRNA to be amplified

## Slide 30: gBlocks – Gene Fragments
Artificial templates of target genes of interest
  Sequence-verified dsDNA in lengths of 125-2000 bp
  Function like PCR products from cloning
Multiple standard curves can be generated from a single template
Combine with multiplexing probes to generate multiple standard curves from a single run

## Slide 31
THE REST OF THE PREVIOUS PRESENTATION

## Slide 32: Bacterial Transformation – Plasmid Map
Linear dsDNA until ligation
  T – overhangs
Ampicillin resistance
Origin of replication
LacZ gene
  ß-galactosidase
  Breaks down lactose/X-gal

## Slide 33: Bacterial Transformation – Plasmid Ligation
T-4 DNA ligase
  Repairs nicks in DNA
Imperfect repair
LacZ gene
  Functional if no insert
  Nonfunctional if DNA inserted
Notes: The shorter the overhang, the lower the Tm
The DNA ligase from bacteriophage T4 is the ligase most-commonly used in laboratory research. Active at 37°C
Repairs nicks in DNA

## Slide 34
Notes: The DNA ligase from bacteriophage T4 is the ligase most-commonly used in laboratory research. Active at 37°C
Repairs nicks in DNA

## Slide 35: Bacterial Transformation – Supercompetent Cells
Genetic Transformation
  Uptake of genetic material from environment
Competent cells
  Capable of transformation
Confers new genetic abilities
  Antibiotic resistance

## Slide 36: Bacterial Transformation – Procedure
Bacteria are to be kept on the bottom shelf of the -80°C freezer
Thawed on ice with ligation mix (plasmids)
Heat shocked
Incubated with LB medium (nutrient media) at 37°C
Plated on agar plates
  X-gal+
  Amplicillin+
Grown overnight at 37°C
Plates placed in incubator upside down (agar on roof) to prevent condensation from dripping onto bacteria
Notes: Very temperature sensitive because the mechanisms by which they work require specific temperatures

## Slide 37: Bacterial Transformation – Mechanisms
Notes: heat-pulse is thought to create a thermal imbalance across the cell membrane, which forces the DNA to enter the cells through either cell pores or the damaged cell wall.
Other methods have used electroporation to create holes in membrane for plasmid to be uptaken
Also incubating them in a solution with divalent cations (CaCl or Mg) helps reduce the number of protein-to-lipopolysaccharide bonds
Increases membrane fluidity, increasing plasmid uptake
DNA entry into E. coli cells is through channels known as zones of adhesion

## Slide 38: Bacterial Transformation – Blue White Screening
Colony principle
  Each colony should arise from an individual bacterium
  Clones
Only bacteria with plasmids should grow
  Ampicillin plated
X-gal
  White if not broken down
  Blue if broken down

## Slide 39: Bacterial Transformation – Plasmid Screening
Individual white colonies selected for further analysis
  Survived ampicillin
  Didn’t break down X-gal
Dipped in PCR mix
  T7 and SP6 primers
  Adds 180 bp to expected insert
Placed in LB broth at 37°C
  Jump start growth
Notes: Autoclaved Toothpicks and pipette tips can be used

## Slide 40: Bacterial Transformation – Culturing Bacteria
Colonies that contain desired plasmid selected
  Grown in much larger volume nutrient medium
  6 mL LB broth with 6 µL ampicillin
Can be grown in massive quantities
  Grams of plasmid instead of ng
Grown overnight at 37°C
  With agitation and tilted at angle
Notes: Lysogeny broth – nutrient media (peptides, vitamins, trace elements, and minerals) yeast extract
incorrectly, taken to mean Luria broth, Lennox broth, orLuria-Bertani medium.
creator Giuseppe Bertani, the abbreviation LB was actually intended to stand for lysogeny broth
Lysogeny, or the lysogenic cycle, is one of two cycles of viral reproduction

## Slide 41: Bacterial Transformation – Plasmid Extraction
Cloudy tubes are spun down
  3000 x g for 10 min
  Pellet formation
Supernatant poured off
  Bleach solution
Cells are lysed
  Column-based isolation of plasmid
  Concentrations in 100s of ng/µL

## Slide 42: Sanger Sequencing – Chain Termination
DNA synthesis proceeds 5’ to 3’
  Relies on 3’ hydroxyl group
Dideoxy termination
  No 3’ hydroxyl
  No nucleophilic attack on phosphate

## Slide 43: Sanger Sequencing – Compnents
Template DNA
  Typically plasmid for us
    1000 ng
Sequence specific primer
Heat stable DNA polymerase
Deoxynucleotide triphosphates
  dATP, dGTP, dTTP, dCTP
Dideoxynucleotide triphosphates
  ddATP, ddGTP, ddTTP, ddCTP
  Typically 1%
  Fluorescently Labeled

## Slide 44: Sanger Sequencing – Fluorescence

## Slide 45: Sanger Sequencing - Results
>Cb-IH-Full-Length-T7
NNNNNNNNNNNNNNANGCNNNNGCCGCCNTGGCGGCCGCGGGAANTCGATTATGAATTATCGAGATGTGAGCAAAGTGCACTTCGGAGGCGACGATGTGTCGCTCTATGGCACTCCCAAGGAGGAGCTGGGACCCGGGCAGCTATGTGTCGGGGCGGCGGGAGCGACGCCCGGGGTAGAGCCGAAACCATCCTTCCTCAAAAACCAGCTACAGGCTCTCTTCCAACCCACCGACAACAGATTAGCCATGAAGCTCTTCGGATCCAAGAAAGCGCTCATGAAAGAGCGCATCAGACAAAAAGCTGCGGGCCACTGGATCATCCATCCCTGCTCCAACTTCAGATTCTACTGGGACCTGTGTATGCTGTTCCTGCTGGTGGCTAACCTGATCATCCTGCCGGTGGCTATCTCCTTCTTCAACGACGACCTCTCCACACGCTGGATCGCCTTCAACTGCCTCTCAGACACAATATTCCTCATAGACATTGTCGTCAATTTTAGAACGGGTATCACGCAACAAGACAATTCCGAACAAGTTATTCTCGACCCCAAGTTAATTGCCAAGCATTACCTTAAGACCTGGTTCTTCCTTGATCTCATCTCCTCGGTGCCACTAGACTACATCTTCCTCATCTTCAACCAGTACCGCGACAAAGAGGACTTCAGCGAGAGTTTCCAGATTCTCCACGCGGGTCGGGCGCTGCGCATCCTCCGCCTGGCCAAGCTGCTCTCCCTGGTCCGCCTCCTCCGCCTCTCCCGGCTGGTCCGATATGTGTCGCAGTGGGAGGAGGTCTATTTCCTCAACATGGCGTCCGTCTTCATGCGCATCTTCAACCTCATCTCCATGATGCTCCTGATTGGCCACTGGTCNNNTGTCTCCAGTTCCTCGTTCCCATGCTGCAGGGCTTTCCCTCCAACTCTTNNNGGCAATCAACGAGCTTCAGAACTCCTACTGGNTANAGCAGTACTCGTGNCGTTCTTCAAGGCCATGTCCCACATGTNNGNANNNNNNNNNNGCTTNCCGNCTNNNANNTCNNCGATCTGNNGCNNNNNCATGATNNNCATGANTTNNGGGGCNNNNNNCTACNCCNNTTTNATNNNNNNNNCNNNNNNNATCNNNCNNNGNANNNATNCCNNNNNNGNNCNNNNNNNNNNNNNNNNNNNNNNNNNNNTNNNNNNNNANNNNNANNNNNNNNGNNNNNTNNNNNNNNNNNNNNCNNNNNNNNNNNNNNNNNNNNCCNNGGNNNNNNNNNNNNNNN
INSERT
PLASMID VECTOR